## Slide 1: Ubiquitous and Secure Networks and Services Redes y Servicios Ubicuos y Seguros
Unit 5: Ubiquitous Systems Security
Lourdes López Santidrián
llopez@diatel.upm.es, lourdes.lopez@upm.es

## Slide 2: Vulnerabilities of ubiquitous networks and services
UNIT 5: Ubiquitous Systems Security

## Slide 3: Why WSN are vulnerable against attacks?
The sensor nodes are constrained by:
  Battery life.
  Computational capabilities.
  Memory.
  Communication band.
Is easy to physically access to nodes:
  Human or machine can reprogram them.
  Human or machine can destroy them.
The communication channel is public.
It is difficult to monitor and control the distributed elements.

## Slide 4: Security Threats
Common Attacks:
  Eavesdropping (passive).
  Data injection (active).
  Message modification (active).
  Message replay (active).
Denial of Service Attacks (DoS):
  Jamming: target the communication channel.
  Power exhaustion: target the nodes.
Node Compromise:
  An attacker can read or modify the internal memory of a node.

## Slide 5: Security Threats
Side-channel Attacks:
  Monitoring of the nodes’ physical properties.
  Acquisition of security credentials (secret keys).
Impersonation Attacks:
  Sybil attack (creation of fake identities).
  Replication attack (creation of duplicate identities).
Protocol-specific Attacks:
  Routing protocols.
    Spoofed Routing Information.
    HELLO Flood Attack.
  Aggregation protocols: falsifying information.
  Time synchronization protocols.

## Slide 6: Security Services
Confidentiality
  Only the desired recipients can understand the message.
  May be not mandatory.
Integrity
  If the data produced and sent over the network are altered, the receiver will have a proof.
  In most cases it is a mandatory feature.

## Slide 7: Security Services
Authentication
  A receiver can verify that the data is really sent by the claimed sender.
  It is mandatory if the network needs a barrier between external and internal members.
Authorization
  It states that only authorized entities can be able to perform certain operations.
Availability
  The users of a WSN must be capable of accessing its services whenever they need them.

## Slide 8: Security Services
Freshness
  The data produced by the WSN must be recent
Forward and Backward Secrecy
  Forward secrecy: where a node should not be able to read any future messages after it leaves the network
  Backward secrecy: where a node is not able to read a previously transmitted message.
Self-organization
  Nodes must be independent and flexible in order to react against problems.

## Slide 9: Security Services
Auditing
  The elements of a WSN must be able to store any events that occur inside the network.
Non-repudiation
  A node cannot deny sending a message, or a recipient cannot deny the reception of a message.
  Evidence that the message was sent is necessary.
Privacy and Anonymity
  The identity of the nodes should be hidden or protected.

## Slide 10: Cryptographic mechanisms as the basis of the security
UNIT 5: Ubiquitous Systems Security

## Slide 11: Secret/Symmetric Key Cryptography
K
A
B
K
m
c = EK (m)
m
c
DK (c) =
DK (EK (m))
Confidentiality
Integrity

## Slide 12: Secret/Symmetric Key Algorithms
Algorithm | Time (ms) | CPU Cycles | Power (μJ) | ROM Memory (Kb)
SkipJack | 2,16 (3) | 15.925,2 (3) | 51,4 (3) | 19 (4)
RC5 | 1,50 (2) | 11.059,2 (1) | 36,00 (1) | 16 (3)
RC6 | 10,78 (5) | 79.478,7 (5) | 258,72 (5) | 16 (3)
TEA | 2,56 (4) | 18.874,4 (4) | 61,44 (4) | 15,5 (1)
XTEA | 1,45 (1) | 12.450,2 (2) | 40,7 (2) | 15,5 (1)
DES | 608,00 (6) | 4.482.662,4 (6) | 14.592,00 (6) | 31 (6)

## Slide 13: Public/Asymmetric Key Cryptography
KSB
A
B
KSA
m
KPA
KPB
….
c = KPB(m)
m
c
KSB (c) =
KSB (KPB (m))
Confidentiality
Authentication
Key agreement

## Slide 14: Public/Asymmetric Key Algorithm
Elliptic Curve Cryptography (ECC)
TinyECC
  ECC-based signature generation and verification (ECDSA).
  Encryption and decryption (ECIES).
  Key Agreement (ECDH).

## Slide 15: Hash Functions
One-way functions:
  If we have m (any size) and H hash function (digital fingerprint):
    h = H(m) with fix size.
  It is almost impossible calculate m from H-1(h)
Can be used to build:
  Message Integrity Code (MIC).
  Message Authentication Code (MAC).
    Authentication.
    Integrity.

## Slide 16: Intrusion DETECTION
UNIT 5: Ubiquitous Systems Security

## Slide 17: Definition of Intrusion Detection
Anomaly detection:
  Analyze the network or system and infer what is “normal” from the analysis.
  Application of statistical or heuristic measures.
  If an event isn’t “normal”  generate an alert
Misuse detection:
  Know what an “attack” is.
  Detection of “attacks”.

## Slide 18: ID Components for WSN
Neighbor monitoring
  Watchdog.
Data fusion
  Local: neighboring nodes.
  Global: overlapping areas.
Topology discovery.
Route tracing.
History.

## Slide 19: Security management
UNIT 5: Ubiquitous Systems Security

## Slide 20: Key Management
Key Management Systems (KMS):
  Creation.
  Distribution.
  Maintenance of secret keys.
IEEE 802.15.4 does not specify how secret keys should be exchanged.
A key-exchange protocol is needed:
  “Key pool” Framework.
  Mathematical Framework.
  Negotiation Framework.
  Public Key Framework.

## Slide 21: Security at WSN Standards
IEEE 802.15.4-2066 security:
  Confidentiality: HW support for AES-128.
  Integrity: MIC or MAC.
  Received Message Authentication: Access Control List (ACL).
ZigBee 2006 and 2007 security:
  Standard Security.
  Confidentiality and Authentication at NWK and APS levels.
  “All nodes on the network trust each other”.
ZigBee PRO security:
  High Security.
  Master key for Symmetric-Key-Key-Exchange.